## Slide 1
Design, run, and analyze behavioral experiments in MATLAB
REPOSITORY OVERVIEW
EPsych v2
A MATLAB toolbox for behavioral experiments — protocol design, session runtime, hardware I/O, stimulus generation, and online analysis in one repository.
976
COMMITS
2019
FIRST COMMIT
GPL-3.0
LICENSE
Daniel Stolzberg, PhD · github.com/dstolz/epsych2
Notes: EPsych v2 is an actively used laboratory toolbox, not a greenfield framework. This deck maps what is in the repository and how the pieces fit together.

## Slide 2
ORIENTATION
What EPsych is
One repository, one workflow. Protocol authoring, a session runtime GUI, a hardware abstraction layer, stimulus generation and calibration, and online psychophysics all ship together.
Built for TDT auditory labs, not locked to them. The protocol file records which backend an experiment uses, and the runtime is written against a single hw.Interface contract, so rigs are swappable.
An evolved tool, by design. Legacy procedural code, GUIDE-era GUIs, and newer object-oriented runtime components coexist. That mixed structure is the key architectural fact to grasp before making changes.
Extensible without forking. Trial selectors, save functions, box GUIs, and analysis classes are all pluggable through documented seams.
~89K
lines of MATLAB
excluding submodule
124
class definitions
across 9 packages
7
hardware backends
one shared contract
56
documentation pages
plus a project wiki
THE PACKAGES UNDER obj/
+epsych
+hw
+gui
+psychophysics
+stimbridge
+teensy
+peripherals
+util
+eplog
stimgen · submodule
Notes: The headline: broad scope, deliberately layered, and honest about being a mixed-vintage codebase.

## Slide 3
THE USER'S PATH
Four stages, from protocol to result
Most of the repository exists to support one of these four stages.
1
Design a protocol
Protocol Designer — conditions, pairing, triggers, compiled to an .eprot file
→
2
Configure subjects
RunExpt GUI — load the protocol, add subjects, pick the hardware backend
→
3
Run the session
Runtime dispatches trials to TDT, Teensy or Bpod; Box GUIs track behavior live
→
4
Analyze the data
BitMask decoding, d′, staircase and threshold estimates from saved sessions
epsych_startup
prepares MATLAB
epsych.ProtocolDesigner
prepares the protocol
epsych.RunExpt
runs the session
Notes: If a new user remembers only one thing, it is this three-command sequence. Design, configure, run, analyze.

## Slide 4
LAYERED VIEW
Architecture at a glance
GUIS
Protocol Designer
RunExpt
Box GUIs
Phase Selector
Staircase Training
↓
EPSYCH CORE
Protocol
Runtime
TrialSelector
BitMask
Events
Trial dispatch, parameter queries, session state, data save
STIMGEN · SUBMODULE
StimType
StimPlay
StimCalibration
Stimulus objects and calibration, via the stimbridge seam
PSYCHOPHYSICS
Staircase
BestPEST
MLP
Detection
Online and offline threshold estimation
↓
HW.INTERFACE
TDT
Teensy
Bpod
Intan RHX
VlcRecorder
one backend contract, swappable rigs
GUIs sit on top; stimgen is a submodule with no dependency on EPsych, reached only through the stimbridge seam; every rig lands on one backend contract.
Notes: Four layers: GUIs, the EPsych core plus stimgen and psychophysics, and the hardware interface beneath. The dependency arrow never runs from stimgen back into EPsych.

## Slide 5
DATA MODEL
The protocol is the experiment
epsych.Protocol is the central data model, serialized to an .eprot file.
WHAT A PROTOCOL CAPTURES
Interfaces — the hw.Interface objects, always including at least one hw.Software design-time parameter store
Options — trial selector class (trialFunc), compileAtRuntime, IncludeWAVBuffers, ConnectionType
COMPILED — the trial table produced by compile(): parameters, trials, writeparams, ntrials
meta — format version, EPsych version, and a protocolVersion string bumped on every save
WHAT ENDS UP ON DISK
.eprot protocols (legacy .prot still loads) · .ecfg session configs, so a whole setup reloads in one step · JSON phase files for named parameter sets that switch training stages without editing the protocol.
COMPILATION
compile() expands the cross-product of unpaired parameter levels into the trials matrix. Paired parameters advance together.
Several parts of the codebase depend on the compiled structure being stable — changes to its format have wide impact.
PARAMETER EXPRESSIONS
A parameter can reference another — Param.Prop or Module.Param.Prop.
On String and StimType parameters the result is a 1-based index into Values instead of the value itself.
Notes: The protocol owns hardware, options, the compiled trial table, and versioning metadata. Compilation is a cross-product over unpaired parameter levels.

## Slide 6
EXECUTION
Runtime and the trial lifecycle
NOCONFIG
›
CONFIGLOADED
›
READY
›
RUNNING
›
POSTRUN
›
STOP
PRGMSTATE — ERROR is reachable from any state.
TIMER CALLBACK CHAIN
1
ep_TimerFcn_Start
Build RUNTIME.TRIALS, create selectors, resolve the CORE trigger parameters, and dispatch the first trial.
2
ep_TimerFcn_RunTime
Poll the TrialComplete trigger; on completion append data to the crash-recovery file, pick the next trial, dispatch it.
3
ep_TimerFcn_Stop
Return interfaces to Idle, broadcast ModeChange, tear down HELPER, save via the configured save function.
4
ep_TimerFcn_Error
Handle timer errors while preserving collected data.
SWAPPABLE
The callback names are configured per session in RunExpt's Customize dialog, so a paradigm can substitute its own timer functions without touching core runtime files.
Hardware interfaces stay connected across reruns within one session.
Notes: A MATLAB timer drives the session. Start builds the trial list and dispatches trial one; RunTime polls for completion and dispatches the next.

## Slide 7
COMMUNICATION
Everything reacts to events
epsych.Helper is the broadcaster on Runtime.HELPER. GUIs and analysis objects subscribe rather than poll.
NewTrial
A new trial begins and parameters are written to hardware.
payload epsych.TrialsData
NewData
A trial completed; listeners fold in the result.
payload epsych.TrialsData
ModeChange
The session changed mode — run, pause, standby, stop.
payload epsych.eventModeChange
WHO IS LISTENING
psychophysics.Psych subclasses — constructed with a Runtime, they update results trial by trial
gui.OnlinePlot, gui.Performance, gui.PsychPlot, gui.History — real-time visualization
gui.BoxGUI subclasses — receive onNewTrial / onNewData / onModeChange hooks; the base class owns listener lifecycle and teardown
Custom paradigm code in cl/ — the reference pattern for extending the runtime without modifying it
WHY IT MATTERS
New analysis or visualization attaches to a running session without any change to the trial loop.
Notes: Three events on one broadcaster. This is the extension point that keeps the trial loop untouched when a lab adds its own analysis.

## Slide 8
ABSTRACTION
One contract, many rigs
Every backend inherits from hw.Interface. Code reads and writes through hw.Parameter, never through a backend-specific API.
THE hw.Interface CONTRACT
connect / disconnect
get_parameter / set_parameter
trigger
setup_interface()
getCreationSpec()
hw.TDT_RPcox
Direct RPvds circuit control; auto-discovers circuit tags
hw.TDT_Synapse
TDT Synapse API; auto-discovers gizmo parameters
in progress
hw.Software
In-memory backend — design-time store and hardware-free testing
hw.Teensy
Teensy 4.x over USB serial; firmware in firmware/EPsychTeensy
in progress
hw.Bpod
Bpod 0.5/0.6 state machine, speaking the firmware byte protocol
in progress
hw.Intan_RHX
Intan RHX electrophysiology over TCP
in progress
hw.VlcRecorder
Webcam preview and recording via a VLC process
Adding a backend touches four hardcoded registry sites outside the class folder — there is no reflection.
Notes: Seven concrete backends today, four still under development. The registry caveat is the most common trap when adding an eighth.

## Slide 9
SUBMODULE BOUNDARY
Stimulus generation lives elsewhere
obj/stimgen is a git submodule pinned to an exact commit of dstolz/stimgen, released independently of this repository.
A ONE-WAY DEPENDENCY
stimgen has no dependency on EPsych. Nothing inside it names an epsych.* or hw.* type — the two classes that translate live in obj/+stimbridge/.
stimbridge.RuntimeHost
implements stimgen.HardwareHost over Runtime / Protocol
stimbridge.InterfaceAdapter
implements the calibration HwAdapter over an hw.Interface
Clone with --recurse-submodules — skipping it degrades protocols silently.
THE SIGNAL PIPELINE
update_signal() implemented by each subclass
apply_normalization() scale to [-1, 1]
apply_calibration() SPL → voltage, lookup table and EQ
apply_gate() cosine-squared onset/offset window
Signal the final waveform
Calibration precedes gating: apply_calibration renormalizes before scaling to the lookup-table voltage, which would undo an earlier ramp.
Guarded by the self-test. Check A3 verifies the pinned commit still satisfies the stimbridge contract, and EPsychInfo.stimgenChksum records it in saved session metadata.
Notes: The submodule boundary is a real architectural constraint, not a packaging detail. Cloning without --recurse-submodules degrades protocols silently, which is why startup warns.

## Slide 10
RESULTS
Psychophysics, online and offline
psychophysics.Psych subclasses run the same code either way — live against a Runtime, or post-hoc against a saved DATA struct array.
ONLINE
Construct with a Runtime. The object subscribes to HELPER.NewData and updates trial by trial while the session runs.
OFFLINE
Construct with a saved per-trial DATA struct array to compute the same results after the fact.
THE ALGORITHMS
Detection
Hit rate, false alarm rate, and d′ from signal detection theory
Staircase
Reversal detection and threshold estimation
BestPEST
Maximum-likelihood threshold tracking
MLP
Bayesian maximum-likelihood estimation with sweet-point placement
OUTCOME ENCODING
epsych.BitMask is a uint32 enumeration encoding trial outcomes — Hit, Miss, CR, FA, and the rest — in a single packed value that every analysis class decodes the same way.
Notes: One class hierarchy serves live monitoring and post-hoc analysis, which is why the same threshold numbers appear during and after a session.

## Slide 11
INTERFACE LAYER
The GUIs a lab actually touches
AUTHORING & CONTROL
epsych.ProtocolDesigner
Build and edit protocols; compile and preview trials
epsych.RunExpt
Subjects, protocols, session state, run/stop; saves .ecfg configs
epsych.SelfTest
Nine headless pre-flight check groups, with a GUI in the Help menu
LIVE MONITORING
gui.OnlinePlot · gui.Performance
Trial-by-trial traces and running performance
gui.PsychPlot · gui.ParameterScatter
Psychometric fits and generic X/Y/color scatter
gui.StaircaseTraining · gui.PhaseSelector
Training control and JSON parameter phases
CUSTOM BOX GUIs
gui.BoxGUI is the abstract base for per-experiment GUIs — lifecycle, event listeners, position preferences, registry teardown, and parameter wiring.
A subclass writes build(fig) and the event hooks. Nothing else.
examples/customgui/
ALSO IN obj/+gui/
History · ModeIndicator · StatusBar · Triggers · ElapsedTrialTimer · FilenameValidator · MicrophonePlot · Parameter_Control / _Monitor / _Update
Notes: The GUI layer is where labs diverge most, so BoxGUI absorbs the boilerplate and leaves subclasses with one method to write.

## Slide 12
FOR DEVELOPERS
Where to plug in
Four common extensions, each with a reference implementation already in the repository.
1
Add a hardware backend
Subclass hw.Interface; implement setup_interface, connect, get/set_parameter, trigger, and a static getCreationSpec.
Then register it in four sites outside the class folder — omitting Protocol.createInterfaceFromStruct_ fails silently.
obj/+hw/@Software/ · documentation/hw/hw_Interface_Tutorial.md
2
Add a stimulus type
Subclass stimgen.StimType in the submodule; implement update_signal() and declare IsMultiObj, CalibrationType, Normalization.
The base class handles gating, normalization, and calibration. Commit to the stimgen repo, then bump the pointer here.
obj/stimgen/+stimgen/Tone.m · Noise.m
3
Add an online analysis
Subclass psychophysics.Psych and implement update(); wire a listener to Runtime.HELPER.NewData.
Optionally pair it with a visualization class in obj/+gui/.
obj/+psychophysics/@Detection/ · obj/+gui/@OnlinePlot/
4
Add a paradigm
Custom trial selector, save function, and box GUI — no core runtime files are modified.
Subscribe to Helper events and swap the timer callbacks from RunExpt's Customize dialog.
cl/ · examples/customgui/ · runtime/savefcns/
Notes: The repository is meant to be extended at these four seams rather than forked. Each row names an existing class to copy.

## Slide 13
GETTING STARTED
Clone, start up, design, run
git clone --recurse-submodules
https://github.com/dstolz/epsych2.git
addpath('C:\path\to\epsych2')
epsych_startup
epsych.ProtocolDesigner
epsych.RunExpt
Skipping the submodule step does not fail loudly — protocols with stimulus objects load with degraded placeholder values. epsych_startup warns when it detects this.
WHERE TO READ NEXT
Installation_Guide.md prerequisites and setup
Toolbox_Overview.md orientation for experimenters
Architecture_Overview.md internals, for developers
RunExpt_GUI_Overview.md a session, walked through
Class_Map.md classes and dependencies
epsych2/wiki the guided companion, two paths
Daniel Stolzberg, PhD · daniel.stolzberg@gmail.com · GNU GPL v3.0
Notes: Three commands get a new user to a running GUI. The submodule warning is the single most common setup failure.